## Slide 1: Updates to the Federal Worker Protection Standard

## Slide 2: Goals of the Revised WPS
Improve occupational protections
Reduce acute occupational pesticide exposures and incidents
Reorganize and streamline the rule
Address concerns related to 1992 WPS
Notes: Occupational Protections for Workers/Handlers
to make it easier to understand
that was enacted in 1995

## Slide 3: The Principles of the Worker Protection Standard
Inform
Protect
Mitigate
about pesticide safety
from potential pesticide exposure
pesticide exposures when they do occur

## Slide 4: Rules Meant to Inform
Pesticide safety training
Trainer requirements/ Training material requirements
Posted pesticide safety information
Pesticide application recordkeeping
Pesticide application notification requirements

## Slide 5: Rules Meant to Inform Updates to Pesticide Safety Training
Worker training 23 points
Handler training 36 points
Annual Training
Emphasis on hazards to pregnant women and small children
No Grace Period
Notes: Pesticide Safety Training is now annual and includes additional points mostly regarding the hazards of pesticides to pregnant women and small children
Worker Training expanded to 23 points
Hander Training expanded to 36 points

## Slide 6: Rules Meant to Inform Updates for Trainers / Training of Handlers or Workers
Certified applicators, or
Trainers who have completed an EPA approved train-the-trainer program, or
A trainer designated by a State/Tribe/EPA
Training Materials EPA Approved
Trainer has to be present throughout training
Notes: Trainers of Workers or Handlers must be:
Certified applicators,
Trainers who have completed an EPA approved train-the-trainer program,
Or a trainer designated by a State/Tribe/EPA
All training materials used must now be EPA approved- new training materials will come out
Trainer has to be present throughout the training to answer questions

## Slide 7: Rules Meant to Inform Updates to Posted Safety Information
SDS for all pesticides applied must be kept in a location accessible to workers and handlers
Notes: SDS for all pesticides applied at the facility must be kept in a location accessible to workers and handlers
These SDS have to be kept for 2 years

## Slide 8: Rules Meant to Inform Updates to Pesticide Recordkeeping
Workers/Handlers must be able to obtain information about pesticide applications and SDS sheets that occurred when they are/were employed
Worker/Handler may also designate a person in writing to have access to this information
Facilities must now keep pesticide application records, SDS, training records for two years
Notes: Workers/Handlers must be able to obtain information about pesticide applications and SDS sheets that occurred when they are/were employed
Worker/Handler may also designate a person in writing to have access to this information
Facilities must now keep pesticide application records, SDS, training records for two years

## Slide 9: Rules Meant to Inform Updates for Pesticide Application Posting
Outdoor Applications
REI Greater than 48 hours
Enclosed Space Application
REI Greater than 4 hours
Notes: The sign must now be posted, instead having the choice between oral notification and posting if an REI is greater than 48 hours for outdoor production.
In enclosed space production, the enclosed space only needs to be posted if the applied product has an REI of greater than 4 hours, in the past, all applications had to be posted.
Post on the border of any worker housing within 100 feet of the treated area.
Must post prior to but no earlier than 24 hours before application (not a change).
Signs must be removed or covered within three days of the end of the application or REI, unless workers are kept out.

## Slide 10: Rules Meant to Protect
Minimum Age
Application Exclusion Zone (AEZ)
Instruction for early-entry workers
Respiratory protection

## Slide 11: Updates to Rules Meant to Protect Minimum Age
Handlers
Early-Entry Workers
Members of Owner’s Immediate Family Exempt
Notes: Minimum Age of 18 does not apply to family members of the facility’s owner

## Slide 12: Updates to Rules Meant to Protect Application Exclusion Zone
0, 25, or 100 feet
Applicators must suspend application whenever someone who is not involved in the application enters the AEZ
Employers are responsible to keep workers and other people out of the AEZ on their own property
Moves with application
Notes: 0,25,100 feet depending on application method
Red = Application Exclusion Zone
Yellow = Spray Swath
Note The AEZ and Spray Swath should realistically look more like a hotdog/pill shape

## Slide 13
Field
AEZ
Treated Area
When the application is concluded, the AEZ no longer exists.
Spray Area
Updates to Rules Meant to Protect Application Exclusion Zones in Outdoor Production

## Slide 14
Updates to Rules Meant to Protect Application Exclusion Zones On Field Borders
14
SUSPEND!
There are workers from the neighboring field in the AEZ!
EVALUATE!
Can you ask the workers to move somewhere else until you are done with the application?
Yes, they agreed to move!
Proceed with caution.
Neighboring Field
Your Field
When the application is finished the AEZ no longer exists.

## Slide 15
Updates to Rules Meant to Protect Application Exclusion Zones On Field Borders
15
SUSPEND!
There are workers from the neighboring field in the AEZ, and they refuse to move!
EVALUATE!
Can you ensure these workers won’t be contacted through drift?
WIND
Yes, the wind is blowing away from the workers and I can ensure that my application will not contact the workers in the other field.
Proceed with caution.
Neighboring Field
Your Field
When the application is finished the AEZ no longer exists.

## Slide 16: Updates to Rules Meant to Protect Early Entry Workers
Early-Entry Workers must now be informed of:
  information about the pesticide application
  specific task to be performed
  amount of time that the worker is allowed to remain in the treated area
  the PPE required by the label
Notes: Early-Entry Workers must now be informed of:
information about the pesticide application
specific task to be performed
amount of time that the worker is allowed to remain in the treated area the PPE required by the label
You can explain this slide like: “Early entry workers must now be told about the pesticide application that occurred, what they will be doing there, and how long they can safely be in there.” “Also they must be told how to use the PPE they are required to wear while doing the work.”

## Slide 17: Updates to Rules Meant to Protect Respiratory Protection
Be medically cleared
Fit tested
Instructed on use and maintainence
Notes: If your facility applies pesticides that require respirators:
Handlers must:
Be medically cleared
Fit tested
Instructed on how to use and maintain respirator
Make sure that audience doesn’t confuse medically cleared with medically monitored. The handler just needs to cleared by a medical professional that they can safely use a respirator.

## Slide 18: Rules Meant to Mitigate
Decontamination supplies
Information for medical personnel
Notes: Specific requirements for Water for Decontamination:
  1 gallon of water for each worker
  3 gallons for each handler and each early-entry worker; measured at the beginning of the work period
  If handler is mixing/loading a product that requires eye protection, eyeflush water must be immediately available at the mix/load site for handler eye flushing
  If applicator is using a product that requires eye protection, one pint of water must be immediately available to each applicator
Information required to be given to medical personnel includes SDS sheets, pesticide application information, circumstances of exposure

## Slide 19: Updates to Rules Meant to Mitigate Decontamination Supplies
Specific requirements for Water for Decontamination:
  1 gallons per worker
  3 gallons per handler or early-entry worker;
  Measured at the beginning of the work period
If handler is mixing/loading a product that requires eye protection, eyeflush water must be immediately available at the mix/load site for handler eye flushing
If applicator is using a product that requires eye protection, one pint of water must be immediately available to each applicator

## Slide 20: Updates to Rules Meant to Mitigate Information to Medical Personnel
SDS sheets
Application information
Circumstances of exposure
Notes: Employers are required to provide this information in case of a pesticide exposure

## Slide 21: Implementation Timeline
1/2/2017 Compliance Required with Most Revised WPS Requirements Except:
New content in Worker and Hander Training
New content in Pesticide Safety Information Display
Responsibility for Handlers related to the Application Exclusion Zone
1/1/2018 Compliance Required with All WPS Requirements
9/28/2015 Revised WPS final rule signed
11/2/2015 Revised WPS final rule published in the Federal Register.

## Slide 22: Resources
www2.epa.gov/pesticide-worker-safety
www.pesticideresources.org

## Slide 23: Contacts
EPA Headquarters
  Richard Pont
    pont.richard@epa.gov
  Nancy Fitz
    fitz.nancy@epa.gov
EPA Regional Contact
Notes: EPA Contacts
Full Name Location Email Address
Richard Pont HQ pont.richard@epa.gov
Nancy Fitz HQ fitz.nancy@epa.gov
Andrea Szylvian R1 szylvian.andrea@epa.gov
Audrey Moore R2 moore.audrey@epa.gov
Magda Rodriguez-Hunt R3 rodriguez-hunt.magda@epa.gov
Randy Dominy R4 dominy.randy@epa.gov
Justin Mullenix R4 mullenix.justin@epa.gov
Don Baumgartner R5 baumgartner.don@epa.gov
Gerardo Acosta R6 acosta.gerardo@epa.gov
Suzanne Stevenson R8 stevenson.suzanne@epa.gov
Katy Wilcoxen R9 wilcoxen.katy@epa.gov
Fabiola Estrada R9 estrada.fabiola@epa.gov
Derrick Terada R10 terada.derrick@epa.gov